## Slide 1: CS 6304 Project 1 ,Prof. Kanad Basu Team members: JXP220032 Date:20th Mar, 2022
In this project we used GEM5 to model CPU caches.
We model specifically 2 level cache for single X86 ISA CPU with L1 cache varying in size and L2 at 1MB with 1GB Dram space.
We use this as base as most of the desktop CPUs in the industry use the cache sizes similar to our base configuration with a notable difference in those being multicore processors.
We use System Emulation (SE mode) for our simulations. We use used 4 benchmarks from SPEC . The simulations were carried out a windows machine running WSL2 with GEM5 installed and built with (8+1) as CPU config

## Slide 2: Project timeline
This project has 5 parts
Preperation ( Installation of GEM5 , understanding the project)
Finding CPI for different configurations
Optimizing CPI for each benchmark
Defining cost function
Optimizing cache performance /percost
First three parts of the project are done by simulating the CPU and running benchmarks . In the coming slides we define appropriate cost functions and give insights on design optimizations

## Slide 3: Defining the cost function.
Here we purely consider cost for hardware implementation on the basis of rough estimate of number of transistors required.
Usually design optimizations are dependent on many factors that include micro architecture, die cost , testing time and functional requirements of the processor.
For example using an advanced tournament branch predictor may cost more number of transistors than simple two level branch predictor. Having larger Reorder buffer with wider CPU front end may cost more than relatively small CPU even though both have same cache sizes. Hence we only define the cost affected by cache design in this project

## Slide 4: Defining the cost function cntd..
cost of CPU die is directly proportional area and so number of transistors .
The parameters we vary in cache design are associativity(a) and number of sets(s) and block size (b) in (bits not Bytes) and tag bits (t) for each entry
cache size L = s * a * b ( in bits)
In addition to data we need to store tags and data in each line of the cache along with we additional bits per set for replacement policy and additional hardware for updating the replacement policy bits and simultaneously checking tags from each way.
We make an assumption that this additional hardware for largers caches ( > 16kB) is insignificant. i.e O( L ) > O(1).

## Slide 5: Defining the cost function (counting #SRAM cells)
We assume for LRU ( optimal LRU ) implementaion we need a log(a) additional bits where ‘a’ is associativity.
So number of SRAM cells required for a cache L(a,s,b,t)
L(a,s,b,t) = s((b+t)a+ a log a )
For example 2-way cache with 16 tag bits and 1024 sets with 64 block size needs 1024*((64 + 16 )*2+ 2 * log 2) SRAM cells . ( 6T SRAM cells)
= 165888 SRAM cells for 16kiloBytes of data ( 131072 bits).
Note that with tag size ‘t’ and block size ‘b’ (bits) we can address 2^t(b/8)bytes of RAM .

## Slide 6: Results
Chart: CPI vs Cache config ( L1I _L1D_L1_assoc_L2_assoc)
| 32kB_32kB_2_2 | 32kB_32kB_4_4 | 32kB_32kB_8_8 | 64kB_64kB_2_2 | 64kB_128kB_2_1 | 128kB_64kB_2_1 | 128kB_128kB_2_1 | 128kB_128kB_2_2 | 128kB_128kB_4_4 | 128kB_128kB_8_8
402.bzip2 | 1.0709 | 1.1096 | 1.0931 | 1.0924 | 1.0957 | 1.1032 | 1.0876 | 1.0803 | 1.0808 | 1.0845
456.hmmer | 1.0066 | 1.0065 | 1.0066 | 1.0053 | 1.0019 | 1.0054 | 1.0025 | 1.0024 | 1.0023 | 1.0019
458.sjeng | 2.3394 | 2.1682 | 1.8482 | 2.3205 | 2.1566 | 1.988 | 2.1313 | 2.1104 | 1.9227 | 2.1476
470.lbm | 1.8246 | 1.8591 | 1.859 | 1.859 | 1.859 | 1.859 | 1.859 | 1.8591 | 1.8591 | 1.8591

## Slide 7
Chart: CPI vs #SRAM Cells due to L1Cache
| 69074944 | 138412032 | 277348352 | 137887744 | 206831616 | 206831616 | 275251200 | 275251200 | 551550976 | 1105199104
402.bzip2 | 1.0709 | 1.1096 | 1.0931 | 1.0924 | 1.0957 | 1.1032 | 1.0876 | 1.0803 | 1.0808 | 1.0845
456.hmmer | 1.0066 | 1.0065 | 1.0066 | 1.0053 | 1.0019 | 1.0054 | 1.0025 | 1.0024 | 1.0023 | 1.0019
458.sjeng | 2.3394 | 2.1682 | 1.8482 | 2.3205 | 2.1566 | 1.988 | 2.1313 | 2.1104 | 1.9227 | 2.1476
470.lbm | 1.8246 | 1.8591 | 1.859 | 1.859 | 1.859 | 1.859 | 1.859 | 1.8591 | 1.8591 | 1.8591